## Slide 1: Unit 7 Sequential Circuits (Flip Flop, Registers)
College of Computer and Information Sciences
Department of Computer Science
CSC 220: Computer Organization

## Slide 3
SR Flip-Flop
The SR flip-flop, also known as a SR Latch, can be considered as one of the most basic sequential logic circuit possible.
This simple flip-flop is basically a one-bit memory bistable device
It has two inputs,
one which will “SET” the device (meaning the output = “1”), and is labelled S and another which will “RESET” the device (meaning the output = “0”), labelled R.

## Slide 10
Give Examples

## Slide 11
The output of the flip flop would always change on every pulse applied to this data input.
To avoid this an additional input called the “CLOCK” or “ENABLE” input is used to isolate the data input from the flip flop’s latching circuitry after the desired data has been stored. The effect is that D input condition is only copied to the output Q when the clock input is active. This then forms the basis of another sequential device called a D Flip Flop.

## Slide 13
It can be seen from the frequency waveforms above, that by “feeding back” the output from Q to the input terminal D, the output pulses at Q have a frequency that are exactly one half ( ƒ/2 ) that of the input clock frequency, ( ƒIN ). In other words the circuit produces frequency division as it now divides the input frequency by a factor of two (an octave) as Q = 1 once every two clock cycles.

## Slide 14
D Flip Flops as Data Latches
A data latch can be used as a device to hold or remember the data present on its data input, thereby acting a bit like a single bit memory device and IC’s such as the TTL 74LS74 or the CMOS 4042 are available in Quad format exactly for this purpose. By connecting together four, 1-bit data latches so that all their clock inputs are connected together and are “clocked” at the same time, a simple “4-bit” Data latch can be made as shown below.

## Slide 20: Regisrers

## Slide 27
MUX 2 - 1
MUX 2 - 1

## Slide 29
Serial-in to Serial-out (SISO) Shift Register

## Slide 31
Serial
Parallel
MUX 2 - 1
MUX 2 - 1

## Slide 34
 |  |  | S0 | S1
 | No change |  | 0 | 0
Shift left (down |  |  | 1 | 0
 | Shift right (up) |  | 0 | 1
 | Parallel load |  | 1 | 1

## Slide 35: Other types of shift registers
Logical shifts – Standard shifts like we just saw. In the absence of a SI input, 0 occupies the vacant position.
  Left: 0110 -> 1100
  Right: 0110 -> 0011
Circular shifts (also called ring counters or rotates) – The shifted out bit wraps around to the vacant position.
  Left: 1001 -> 0011
  Right: 1001 -> 1100
Switch-tail ring counter (aka Johnson counter) – Similar to the ring counter, but the serial input is the complement of the serial output.
  Left: 1001 -> 0010
  Right: 1001 -> 0100
Arithmetical shifts – Left shifting is the same as a logical shift. Right shifting however maintains the MSB.
  Left: 0110 -> 1100
  Right: 0110 -> 0011; 1011 -> 1101

## Slide 36: Example
Consider a 4-bit register with the following inputs
  parallel data inputs ABCD = 0011
  left serial input LSI = 1 (This is the serial input for a left shift.)
  right serial input RSI = 0 (This is the serial input for a right shift.)
  The three control inputs S2, S1, S0 operate as shown in the table to the right.
  Let the initial register content be QAQBQCQD = 0101
S2 | S1 | S0 | Operation
0 | 0 | 0 | left shift
0 | 0 | 1 | circular left shift
0 | 1 | 0 | right shift
0 | 1 | 1 | circular right shift
1 | 0 | 0 | no change
1 | 0 | 1 | parallel load
1 | 1 | 0 | complement each bit
1 | 1 | 1 | set to 1111

## Slide 37: Example
S2 | S1 | S0 | Operation
0 | 0 | 0 | left shift
0 | 0 | 1 | circular left shift
0 | 1 | 0 | right shift
0 | 1 | 1 | circular right shift
1 | 0 | 0 | no change
1 | 0 | 1 | parallel load
1 | 1 | 0 | complement each bit
1 | 1 | 1 | set to 1111
Other Information |  |  | 
Parallel Load |  |  | ABCD = 0011
LS1 |  |  | 1
RSI |  |  | 0
S2 | S1 | S0 | QA | QB | QC | QD
 |  |  | 0 | 1 | 0 | 1
0 | 0 | 0 |  |  |  | 
0 | 0 | 1 |  |  |  | 
0 | 1 | 0 |  |  |  | 
1 | 0 | 0 |  |  |  | 
0 | 1 | 1 |  |  |  | 
1 | 0 | 1 |  |  |  | 
1 | 1 | 1 |  |  |  | 
0 | 0 | 0 |  |  |  | 
1 | 1 | 0 |  |  |  | 

## Slide 38: Example
S2 | S1 | S0 | Operation
0 | 0 | 0 | left shift
0 | 0 | 1 | circular left shift
0 | 1 | 0 | right shift
0 | 1 | 1 | circular right shift
1 | 0 | 0 | no change
1 | 0 | 1 | parallel load
1 | 1 | 0 | complement each bit
1 | 1 | 1 | set to 1111
Other Information |  |  | 
Parallel Load |  |  | ABCD = 0011
LS1 |  |  | 1
RSI |  |  | 0
S2 | S1 | S0 | QA | QB | QC | QD
 |  |  | 0 | 1 | 0 | 1
0 | 0 | 0 |  |  |  | 
0 | 0 | 1 |  |  |  | 
0 | 1 | 0 |  |  |  | 
1 | 0 | 0 |  |  |  | 
0 | 1 | 1 |  |  |  | 
1 | 0 | 1 |  |  |  | 
1 | 1 | 1 |  |  |  | 
0 | 0 | 0 |  |  |  | 
1 | 1 | 0 |  |  |  | 

## Slide 39: Example
S2 | S1 | S0 | Operation
0 | 0 | 0 | left shift
0 | 0 | 1 | circular left shift
0 | 1 | 0 | right shift
0 | 1 | 1 | circular right shift
1 | 0 | 0 | no change
1 | 0 | 1 | parallel load
1 | 1 | 0 | complement each bit
1 | 1 | 1 | set to 1111
Other Information |  |  | 
Parallel Load |  |  | ABCD = 0011
LS1 |  |  | 1
RSI |  |  | 0
S2 | S1 | S0 | QA | QB | QC | QD
 |  |  | 0 | 1 | 0 | 1
0 | 0 | 0 | 1 | 0 | 1 | 1
0 | 0 | 1 |  |  |  | 
0 | 1 | 0 |  |  |  | 
1 | 0 | 0 |  |  |  | 
0 | 1 | 1 |  |  |  | 
1 | 0 | 1 |  |  |  | 
1 | 1 | 1 |  |  |  | 
0 | 0 | 0 |  |  |  | 
1 | 1 | 0 |  |  |  | 

## Slide 40: Example
S2 | S1 | S0 | Operation
0 | 0 | 0 | left shift
0 | 0 | 1 | circular left shift
0 | 1 | 0 | right shift
0 | 1 | 1 | circular right shift
1 | 0 | 0 | no change
1 | 0 | 1 | parallel load
1 | 1 | 0 | complement each bit
1 | 1 | 1 | set to 1111
Other Information |  |  | 
Parallel Load |  |  | ABCD = 0011
LS1 |  |  | 1
RSI |  |  | 0
S2 | S1 | S0 | QA | QB | QC | QD
 |  |  | 0 | 1 | 0 | 1
0 | 0 | 0 | 1 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1 | 1 | 1
0 | 1 | 0 |  |  |  | 
1 | 0 | 0 |  |  |  | 
0 | 1 | 1 |  |  |  | 
1 | 0 | 1 |  |  |  | 
1 | 1 | 1 |  |  |  | 
0 | 0 | 0 |  |  |  | 
1 | 1 | 0 |  |  |  | 

## Slide 41: Example
S2 | S1 | S0 | Operation
0 | 0 | 0 | left shift
0 | 0 | 1 | circular left shift
0 | 1 | 0 | right shift
0 | 1 | 1 | circular right shift
1 | 0 | 0 | no change
1 | 0 | 1 | parallel load
1 | 1 | 0 | complement each bit
1 | 1 | 1 | set to 1111
Other Information |  |  | 
Parallel Load |  |  | ABCD = 0011
LS1 |  |  | 1
RSI |  |  | 0
S2 | S1 | S0 | QA | QB | QC | QD
 |  |  | 0 | 1 | 0 | 1
0 | 0 | 0 | 1 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 |  |  |  | 
0 | 1 | 1 |  |  |  | 
1 | 0 | 1 |  |  |  | 
1 | 1 | 1 |  |  |  | 
0 | 0 | 0 |  |  |  | 
1 | 1 | 0 |  |  |  | 

## Slide 42: Example
S2 | S1 | S0 | Operation
0 | 0 | 0 | left shift
0 | 0 | 1 | circular left shift
0 | 1 | 0 | right shift
0 | 1 | 1 | circular right shift
1 | 0 | 0 | no change
1 | 0 | 1 | parallel load
1 | 1 | 0 | complement each bit
1 | 1 | 1 | set to 1111
Other Information |  |  | 
Parallel Load |  |  | ABCD = 0011
LS1 |  |  | 1
RSI |  |  | 0
S2 | S1 | S0 | QA | QB | QC | QD
 |  |  | 0 | 1 | 0 | 1
0 | 0 | 0 | 1 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 |  |  |  | 
1 | 0 | 1 |  |  |  | 
1 | 1 | 1 |  |  |  | 
0 | 0 | 0 |  |  |  | 
1 | 1 | 0 |  |  |  | 

## Slide 43: Example
S2 | S1 | S0 | Operation
0 | 0 | 0 | left shift
0 | 0 | 1 | circular left shift
0 | 1 | 0 | right shift
0 | 1 | 1 | circular right shift
1 | 0 | 0 | no change
1 | 0 | 1 | parallel load
1 | 1 | 0 | complement each bit
1 | 1 | 1 | set to 1111
Other Information |  |  | 
Parallel Load |  |  | ABCD = 0011
LS1 |  |  | 1
RSI |  |  | 0
S2 | S1 | S0 | QA | QB | QC | QD
 |  |  | 0 | 1 | 0 | 1
0 | 0 | 0 | 1 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 1 | 0 | 0 | 1
1 | 0 | 1 |  |  |  | 
1 | 1 | 1 |  |  |  | 
0 | 0 | 0 |  |  |  | 
1 | 1 | 0 |  |  |  | 

## Slide 44: Example
S2 | S1 | S0 | Operation
0 | 0 | 0 | left shift
0 | 0 | 1 | circular left shift
0 | 1 | 0 | right shift
0 | 1 | 1 | circular right shift
1 | 0 | 0 | no change
1 | 0 | 1 | parallel load
1 | 1 | 0 | complement each bit
1 | 1 | 1 | set to 1111
Other Information |  |  | 
Parallel Load |  |  | ABCD = 0011
LS1 |  |  | 1
RSI |  |  | 0
S2 | S1 | S0 | QA | QB | QC | QD
 |  |  | 0 | 1 | 0 | 1
0 | 0 | 0 | 1 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 1 | 0 | 0 | 1
1 | 0 | 1 | 0 | 0 | 1 | 1
1 | 1 | 1 |  |  |  | 
0 | 0 | 0 |  |  |  | 
1 | 1 | 0 |  |  |  | 

## Slide 45: Example
S2 | S1 | S0 | Operation
0 | 0 | 0 | left shift
0 | 0 | 1 | circular left shift
0 | 1 | 0 | right shift
0 | 1 | 1 | circular right shift
1 | 0 | 0 | no change
1 | 0 | 1 | parallel load
1 | 1 | 0 | complement each bit
1 | 1 | 1 | set to 1111
Other Information |  |  | 
Parallel Load |  |  | ABCD = 0011
LS1 |  |  | 1
RSI |  |  | 0
S2 | S1 | S0 | QA | QB | QC | QD
 |  |  | 0 | 1 | 0 | 1
0 | 0 | 0 | 1 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 1 | 0 | 0 | 1
1 | 0 | 1 | 0 | 0 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1
0 | 0 | 0 |  |  |  | 
1 | 1 | 0 |  |  |  | 

## Slide 46: Example
S2 | S1 | S0 | Operation
0 | 0 | 0 | left shift
0 | 0 | 1 | circular left shift
0 | 1 | 0 | right shift
0 | 1 | 1 | circular right shift
1 | 0 | 0 | no change
1 | 0 | 1 | parallel load
1 | 1 | 0 | complement each bit
1 | 1 | 1 | set to 1111
Other Information |  |  | 
Parallel Load |  |  | ABCD = 0011
LS1 |  |  | 1
RSI |  |  | 0
S2 | S1 | S0 | QA | QB | QC | QD
 |  |  | 0 | 1 | 0 | 1
0 | 0 | 0 | 1 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 1 | 0 | 0 | 1
1 | 0 | 1 | 0 | 0 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1
0 | 0 | 0 | 1 | 1 | 1 | 1
1 | 1 | 0 |  |  |  | 

## Slide 47: Example
S2 | S1 | S0 | Operation
0 | 0 | 0 | left shift
0 | 0 | 1 | circular left shift
0 | 1 | 0 | right shift
0 | 1 | 1 | circular right shift
1 | 0 | 0 | no change
1 | 0 | 1 | parallel load
1 | 1 | 0 | complement each bit
1 | 1 | 1 | set to 1111
Other Information |  |  | 
Parallel Load |  |  | ABCD = 0011
LS1 |  |  | 1
RSI |  |  | 0
S2 | S1 | S0 | QA | QB | QC | QD
 |  |  | 0 | 1 | 0 | 1
0 | 0 | 0 | 1 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 1 | 0 | 0 | 1
1 | 0 | 1 | 0 | 0 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1
0 | 0 | 0 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0 | 0 | 0